## Slide 1: Image Formation
Topic 1 of Part I
Image Formation
CSc I6716
Fall 2023
Zhigang Zhu, City College of New York zzhu@ccny.cuny.edu
Notes: This course is a basic introduction to parts of the field of computer vision. This version of the course covers topics in 'early' or 'low' level vision and parts of 'intermediate' level vision. It assumes no background in computer vision, a minimal background in Artificial Intelligence and only basic concepts in calculus, linear algebra, and probability theory.

## Slide 2: Acknowledgements
The slides in this lecture were kindly provided by
Professor Allen Hanson
University of Massachusetts at Amherst

## Slide 3: Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 4: Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 5: Abstract Image
An image can be represented by an image function whose general form is f(x,y).
f(x,y) is a vector-valued function whose arguments represent a pixel location.
The value of f(x,y) can have different interpretations in different kinds of images.
Examples
Intensity Image - f(x,y) = intensity of the scene
Range Image - f(x,y) = depth of the scene from imaging system
Color Image - f(x,y) = {fr(x,y), fg(x,y), fb(x,y)}
Video - f(x,y,t) = temporal image sequence

## Slide 6: Basic Radiometry
Radiometry is the part of image formation concerned with the relation among the amounts of light energy emitted from light sources, reflected from surfaces, and registered by sensors.
Notes: Radi-ometry

## Slide 7: Light and Matter
The interaction between light and matter can take many forms:
  Reflection
  Refraction
  Diffraction
  Absorption
  Scattering

## Slide 8: Lecture Assumptions
Typical imaging scenario:
  visible light
  ideal lenses
  standard sensor (e.g. TV camera)
  opaque objects
Goal
To create 'digital' images which can be processed to recover some of the characteristics of the 3D world which was imaged.
Notes: Our goal is to trace the mechanisms of image formation from light emitted from a source, through the interaction of the light with a surface, to the incidence of light on a sensor, and finally to the conversion of the sensor output to a discrete representation of the light patterns arising from the scene - the result is called a digital image. In order to get a sense of how this works, we make some simplifying assumptions:
- only light visible to you and me is considered.
- all lenses are ideal in that they have no geometric distortions and transmit all of the light impinging on them.
- a standard sensor, such as a TV camera, is assumed throughout.
- all objects in the scene are opaque (although this is not a strict limitation on the presentation.

## Slide 9: Image Formation
Notes: Let's start with an overview of the process up to the creation of the signal. For the sake of the example, we assume that the light source is the sun, the surface represents a small portion of the surface of an object, and the optical system is composed of a simple pinhole lens. Light from the sun is incident on the surface, which in turn reflects some of the incident light. Part of the light reflected from the surface is captured by the pinhole lens and is projected onto the imaging plane.
The point on the imaging plane represented by the dot corresponds to the image location of the corresponding point on the surface. Clearly a different point on the imaging plane would correspond to a different point on the surface.
If the imaging plane is a piece of black and white film, as in a real camera, the representation of the intensity of the light reflecting from the surface is recorded by the silver density in the negative. The more light reflected from the surface, the denser the silver grains in the film become. When the negative is then printed, the corresponding location is bright, since the dense silver grains reduce the amount of light reaching the photographic paper surface.
In the case of color film, three separate silver emulsions are used. Each emulsion is selectively sensitive to light of different frequencies: red, green, and blue. From these three color components, the full spectrum of color available in the original scene can be reconstructed. Note that this is not strictly true; there are colors which cannot be reconstructed in this way due to limitations in the color dyes available. When the three emulsions are printed on color sensitive paper containing three layers, we get the familiar color print.
In the case of a black and white TV camera, the intensity of the light is coded in the amplitude of the electrical signal produced by the camera. For color TV cameras, the signal contains values for the red, green, and blue components of the incident light at a point.

## Slide 10: Steps
World Optics Sensor
Signal Digitizer
Digital Representation
World reality
Optics focus {light} from world on sensor
Sensor converts {light} to {electrical energy}
Signal representation of incident light as continuous electrical energy
Digitizer converts continuous signal to discrete signal
Digital Rep. final representation of reality in computer memory
Notes: A digital image is created when a sensor records (light) energy as a two-dimensional function which is then converted to a discrete representation. There are a number of steps in this creation process. Again, we assume a typical imaging scenario. Assuming that objects in the world are illuminated by a source of light, the light reflected by the objects is gathered by an optical system and focused on a sensor. The role of the sensor is to convert the pattern of light into a two-dimensional continuous signal (typically electrical in nature). Both the two-dimensional extent of the signal and its amplitude must then be converted into a discrete form. From the point of view of a vision system, the resulting set of numbers represents the system's internal representation of the world.
Each of these steps introduces various forms of distortion and degradation into the signal; consequently, each step has interesting problems that need to be considered.

## Slide 11: Factors in Image Formation
Geometry
  concerned with the relationship between points in the three-dimensional world and their images
Radiometry
  concerned with the relationship between the amount of light radiating from a surface and the amount incident at its image
Photometry
  concerned with ways of measuring the intensity of light
Digitization
  concerned with ways of converting continuous signals (in both space and time) to digital approximations
Notes: During the l970's, there were a group of researchers in the vision field who felt that if we thoroughly understood geometry, radiometry, and photometry, then the field would be well along the path to understanding how to build vision systems. While an understanding of these areas is important to vision, it has become abundantly clear that there is much more to understand about vision.
Image geometry relates points in the three dimensional world to their projection in the image plane. This effectively provides us with the spatial relationship between points on the sensor(s) surface and points in the world. Two types of projection models are typically used: perspective projection and orthographic projection. Perspective projection is what we normally see in photographs; the effect of perspective projection is to make railroad tracks look narrower as they recede from the viewer. Orthographic projection is an approximation to perspective projection when the viewpoint (sensor) is located at infinity relative to the objects being imaged. In this case, there is no distortion of the coordinates of a point and consequently railroad tracks look parallel in the image.
Radiometry is concerned with the physics of the reflectance of objects and establishes the relationship between light emitted from a source and how much of this light eventually gets to the sensor. This also depends on the imaging geometry, on the characteristics of the optical path through which the light must travel, and on the reflectance of the surfaces of objects in the scene.
Photometry is concerned with mechanisms for measuring the amount of light energy falling on the sensor.
Digitization processes convert the continuous signal from the sensor (which should be proportional to the amount of light incident on it) into a discrete signal. Both the spatial distribution of light and its intensity over the sensor plane must be converted to discrete values to produce a digital image.

## Slide 12: Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 13: Geometry
Geometry describes the projection of:
two-dimensional (2D) image plane.
three-dimensional (3D) world
Typical Assumptions
  Light travels in a straight line
Optical Axis: the axis perpendicular to the image plane and passing through the pinhole (also called the central projection ray)
Each point in the image corresponds to a particular direction defined by a ray from that point through the pinhole.
Various kinds of projections:
  - perspective - oblique
  - orthographic - isometric
  - spherical

## Slide 14: Basic Optics
Two models are commonly used:
  Pin-hole camera
  Optical system composed of lenses
Pin-hole is the basis for most graphics and vision
  Derived from physical construction of early cameras
  Mathematics is very straightforward
Thin lens model is first of the lens models
  Mathematical model for a physical lens
  Lens gathers light over area and focuses on image plane.

## Slide 15: Pinhole Camera Model
World projected to 2D Image
  Image inverted
  Size reduced
  Image is dim
  No direct depth information
f called the focal length of the lens
Known as perspective projection
Notes: In the diagram, f is called the focal length of the (pinhole) lens and is the distance from the center of the lens to the image plane measured along the optical axis. The center of the lens is the point in the lens system through which all rays must pass.
From the diagram, it is easy to see that the image projected onto the image plane is inverted. The ray from the cartoon figure's head, for example, is projected to a point near the bottom of the image plane, while the ray from a point on the figure's foot is projected to a point near the top of the image plane.
Various coordinate reference frames can be associated with the pinhole camera system. In most of them, the Z axis coincides with the optical axis (also called the central projection ray). By convention, the image plane is located at Z = 0 and the lens is located at Z = f. Z is also the distance to an object as measured along the optical axis; also by convention, Z is positive coming out of the camera. The X and Y axis lie in the image place - we will establish exactly how later.
It is possible to reverse the position of the image plane and the camera lens so that the projected image is upright....

## Slide 16: Pinhole camera image
Photo by Robert Kosara, robert@kosara.net
http://www.kosara.net/gallery/pinholeamsterdam/pic01.html
Amsterdam

## Slide 17: Equivalent Geometry
Consider case with object on the optical axis:
More convenient with upright image:
Equivalent mathematically
Notes: These geometries are equivalent mathematically. In the second case, the center of projection is located at -f along the optical axis. The image plane is still considered to be at z=0.
The equivalence of both geometries can be established by recognizing that the two triangles in the upper diagram are similar to the two triangles in the lower diagram. In fact, it is exactly this relationship which will allow us to derive the perspective projection equations.....

## Slide 18: Thin Lens Model
f
IMAGE
PLANE
OPTIC
AXIS
LENS
i
o
1 1 1
f i o
=
+
‘THIN LENS LAW’
Rays entering parallel on one side converge at focal point.
Rays diverging from the focal point become parallel.

## Slide 19: Coordinate System
Simplified Case:
  Origin of world and image coordinate systems coincide
  Y-axis aligned with y-axis
  X-axis aligned with x-axis
  Z-axis along the central projection ray
Notes: We assume a particularly simple relationship between the world coordinate system (X,Y,Z) and the image coordinate system (x,y), as shown in the figure at the bottom of the slide. The origin of the world coordinate system (0,0,0) is assumed to coincide with the origin of the image coordinate system (0,0). Furthermore, we assume that the X-axis of the world coordinate system is aligned with the x-axis of the image coordinate system and that the Y-axis is aligned with the y- axis. Then the Z-axis of the world system is aligned with the optical axis.

## Slide 20: Perspective Projection
Compute the image coordinates of p in terms of the world coordinates of P.
Look at projections in x-z and y-z planes
Notes: Our goal is to compute the image coordinates of the point P located at (X,Y,Z) in the world coordinate system under perspective projection. Equivalently, we want to know where the ray passing through the point P and the center of the camera lens located at -f pierces the image plane. We can do this rather simply by examining the projections of the point P on the (x,Z) and (y,Z) planes.

## Slide 21: X-Z Projection
By similar triangles:
=
x
f
X
Z+f
=
x
fX
Z+f
Notes: Consider the view looking down from a point above the previous figure; equivalently consider the plane Y=0. Then the ray from the projection of point P onto this plane through the lens center must intersect the image plane along the x-axis; this intersection point will give us the x-coordinate of the projection of point P onto the image plane (we'll do the same thing for the y-coordinate in the next slide). From the figure, it is clear that the two shaded triangles are similar. From similar triangles, we know that the ratio x/f must equal X/(Z+f). This equality can then be solved for x.
The resulting formula allows us to compute the x-coordinate of the point P(X,Y,Z). Notice that if f is small compared to Z, then the formula looks like f(X/Z), so what is really happening is that the image coordinate, x, is just the world coordinate X scaled by Z. It is this scaling effect which leads to the phenomena we normally associate with perspective.

## Slide 22: Y-Z Projection
By similar triangles:
=
y
f
Y
Z+f
=
y
fY
Z+f
Notes: The other projection is to the x = 0 plane; otherwise everything is identical to the previous case.

## Slide 23: Perspective Equations
Given point P(X,Y,Z) in the 3D world
The two equations:
transform world coordinates (X,Y,Z)
into image coordinates (x,y)
Question:
  What is the equation if we select the origin of both coordinate systems at the nodal point?
=
y
fY
Z+f
=
x
fX
Z+f

## Slide 24: Reverse Projection
Given a center of projection and image coordinates of a point, it is not possible to recover the 3D depth of the point from a single image.
In general, at least two images of the same point taken from two different locations are required to recover depth.
Notes: We have seen that, given the coordinates of a point (X,Y,Z) and the focal length of the lens f, the image coordinates (x,y) of the projection of the point on the image plane can be uniquely computed. Now let us ask the reverse question: Given the coordinates (x,y) of a point in the image, can we uniquely compute the world coordinates (X,Y,Z) of the point? In particular, can we recover the depth of the point (Z)?
To see that this is not possible, consider the infinitely extended ray through the center of projection and the point (x,y) on the image plane. Any point P in the world coordinate system which lies along this ray will project to the same image coordinates. Thus, in the absence of any additional information about P, we cannot determine its world coordinates from knowledge of the coordinates of its image projection.
However, it is easy to show that if we know the image coordinates of the point P in two images taken from different world coordinate locations, and if we know the relationship between the two sensor locations, then 3D information about the point can be recovered. This is known as stereo vision; in the human visual system, our two eyes produce slightly different images of the scene and from this we experience a sensation of depth.

## Slide 25: Stereo Geometry
Depth obtained by triangulation
Correspondence problem: pl and pr must correspond to the left and right projections of P, respectively.
P(X,Y,Z)
Notes: Binocular (or stereo) geometry is shown in the figure. The vergence angle is the angle between the two image planes, which for simplicity we assume are aligned so that the y-axes are parallel. Given either image of the pair, all we can say is that the object point imaged at Pr or Pl is along the respective rays through the lens center. If in addition we know that Pr and Pl are the image projections of the same object point, then the depth of this point can be computed using triangulation (we will return to this in more detail in the section on motion and stereo).
In addition to the camera geometry, the key additional piece of information in stereo vision is the knowledge that Pr and Pl are projections of the same object point. Given only the two images, the problem in stereo vision is to determine, for a given point in the left image (say), where the projection of this point is in the right image. This is called the correspondence problem. Many solutions to the correspondence problem have been proposed in the literature, but none have proven entirely satisfactory for general vision (although excellent results can be achieved in many cases).

## Slide 26: Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 27: Radiometry
Image: two-dimensional array of 'brightness' values.
Geometry: where in an image a point will project.
Radiometry: what the brightness of the point will be.
  Brightness: informal notion used to describe both scene and image brightness.
  Image brightness: related to energy flux incident on the image plane: => IRRADIANCE
  Scene brightness: brightness related to energy flux emitted (radiated) from a surface: => RADIANCE
Notes: We now turn our attention to the second of the topics in our group of four: radiometry. Recall that radiometry is concerned with establishing the relationship between the amount of light incident on a scene and the fraction of the light which eventually reaches the sensor. This fraction depends upon the characteristics of the light source(s), the characteristics of the objects being imaged, the optical system, and of course the image geometry.
Brightness is a term which is consistently misused in the literature, often used to refer to both scene brightness and image brightness. As we shall see, these are two different entities and in order to be unambiguous, we need to introduce some additional terminology.
The term radiance refers to the energy emitted from a source or a surface. The term irradiance refers to the energy incident on a surface. Consequently, scene irradiance is the light energy incident on the scene or a surface in the scene, and the image irradiance is the light energy incident on the image plane (which is usually the sensor). Image irradiance is the energy which is available to the sensor to convert to a digital image (in our case) or a photographic negative, etc. Scene radiance is the light energy reflected from the scene as a result of the scene being illuminated by a light source.
The treatment of radiometry in these notes closely follows that of Horn in Robot Vision [MIT Press 1986] and in Horn and Sjoberg "Calculating the Reflectance Map", Applied Optics 18:11, June 1979, pp. 1770-1779.

## Slide 28: Radiometry & Geometry
Goal: Relate the radiance of a surface to the irradiance in the image plane of a simple optical system.
Notes: Our goal is to relate the radiance (or luminance) of a surface patch to the irradiance of the projected image of the surface patch on the image plane. We will assume a very simple optical system consisting of a single simple lossless lens of diameter d with a focal length of f. A light ray reflected from the surface passes through the nodal point of the lens and intersects the image plane. A finite amount of energy must be available at the image plane in order to induce a change in photographic film or to generate an electrical signal in a video camera. Consequently, the analysis will assume that a very small patch on a surface in the three-dimensional world is imaged as a small patch on the image plane. If we know the radiance of the surface, what is the energy available (irradiance) at the image plane?
F = power of light source
i = incident angle of light ray
e = emittance angle of light ray
a = angle between emitted ray and optical axis
dAs = area of surface patch
dAi = image area of projected surface patch
z = distance to surface patch along optical axis
f = focal length of lense
d = diameter of lens
Notation

## Slide 29: Radiometry Final Result
Image irradiance is proportional to:
  Scene radiance Ls
  Focal length of lens f
  Diameter of lens d
    f/d is often called the f-number of the lens
  Off-axis angle a
E =
i
s
L
cos a
d
-f
2
p
4
4
Notes: The image irradiance, as we expected it would be, is directly proportional to the scene radiance (the amount of light coming off the surface patch), directly proportional to the diameter of the lens, and inversely proportional to the focal length of the lens. It is a function of the fourth power of the cosine of the angle between the central projection ray and the center of the patch. This means that the light incident on the sensor falls off as the fourth power of the cosine of the angle between the central projection ray and the line between the two patches. Put another way, as the surface patch moves further out in the field of view of the lens, the 'brightness' of the image projection of the patch falls off as the fourth power of the cosine of the angle.

## Slide 30: Cos a Light Falloff
4
x
y
p/2
-p/2
-p/2
Lens Center
Top view shaded by height
Notes: The slide shows a three-dimensional plot of cos 4 a . Since the projection of the lens center usually coincides with the center of the image, you can imagine the plot centered over the image. It then represents the relative 'brightness' of the projection of a unit light source as the source moves away from the center of projection. The second figure shows the same function but viewed from the top and shaded by the 'height' of the function; the center value is 1 and the black areas correspond to 0.
Most optical systems cut off a good portion of the lens with an aperture so that only the central portion of the lens is used. For small values of a , the light distribution is fairly constant. Electronic sensors can be calibrated for the falloff.
The derivation relates scene radiance to image irradiance. The amount of light reaching the image plane is what's available to the sensor to convert to some kind of electrical signal.

## Slide 31: Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 32: Photometry
Photometry:
  Concerned with mechanisms for converting light energy into electrical energy.
World Optics Sensor
Signal Digitizer
Digital Representation
Notes: Thus far, we have examined: the geometry of the imaging system, how this geometry affects the light passing through it (in a somewhat ideal case), how properties of the reflecting surface affect the light reaching the sensor, and have also related the incident illumination to the image irradiance. We now turn out attention (albeit briefly) to different kinds of sensors and how the image irradiance information can be converted to electrical signals (which can then be digitized). There is an abundance of information in the signal detection and signal processing literature on different kinds of sensors and their electrical and geometric properties; consequently, our excursion into this will be brief and highly simplified.

## Slide 33: B&W Video System
Notes: One of the simplest imaging systems consists of a B&W television camera connected to a computer through some specialized electronics. The camera scans the image plane and converts the image irradiance into an electrical signal. Thus, the two-dimensional image signal is converted to a one-dimensional electrical signal in which 2D spatial location (in the image) is encoded in the time elapsed from the start of the scan. TV cameras typically scan the image plane 30 times per second. A single scan of the image plane is made up of 525 lines scanned in two fields - all the odd number lines first followed by the even numbered lines (this is done mainly to prevent visual flicker). The electrical signal at the output of the video camera is proportional to the irradiance incident on the image plane along the scan lines. There are a number of different types of sensors commonly used in video cameras, but they all convert light energy into electrical energy.
The continuous electrical signal must be converted into a discrete two-dimensional array of discrete values (which are proportional to the signal and hence to the irradiance). We'll return to this point later.

## Slide 34: Color Video System
Notes: The situation is very similar for color video systems. The main difference is that these systems contain three sensors which are selectively sensitive to red, green, and blue (see note below). There are now three output signals which must be digitized and quantized into three discrete arrays - one for each of the primary spectral colors.
The study of color, its perception by human observers, and its reproduction in printed and electronic form is very broad and covers many topics, from characteristics of the human visual system and the psychology of color perception, through the study of light sensitive material and their spectral characteristics, to the study of inks and dyes for reproducing color. The approach we will take here is to try to ignore much of this work, discussing only the concepts important to our understanding of other aspects of computer vision. You are warned, however, that there is a vast amount of material available on color, much of it fascinating, and what we do here is usually a drastic simplification of the actual case.
__________________________note__________________________
In general any three widely spaced colors can be chosen - these effectively become the 'basis' set of colors in the same sense as the basis vectors for a vector space. All colors reproducible by the system are combinations of these basis colors. Recall that a set of vectors is a basis of a vector space if and only if none of the vectors can be expressed as a linear combination of the remaining vectors.

## Slide 35: Color Representation
Color Cube and Color Wheel
For color spaces, please read the following (the apps might not work)
  Color Cube https://www.colorcube.com/
  Color Wheel http://r0k.us/graphics/SIHwheel.html
R
B
G
S
I
H

## Slide 36: Digital Color Cameras
Three CCD-chips cameras
  R, G, B separately, AND digital signals instead analog video
One CCD Cameras
  RGB “Bayer” Color and MicroLenses
  http://www.siliconimaging.com/RGB%20Bayer.htm
Notes: Image Format with Matlab (in Homework 1 before 2007)

## Slide 37: Human Eyes & Color Perception
Visit a cool site with Interactive Java tutorial:
  Human Vision and Color Perception
Notes: Visit a cool site with Interactive Java tutorial:
  http://micro.magnet.fsu.edu/primer/lightandcolor/vision.html
There are shifts in color sensitivity with variations in light levels so blue colors look relatively brighter in dim light and red colors look brighter in bright light.
Another site about human color perception:
  http://www.photo.net/photo/edscott/vis00010.htm
  The sensitivity curves of the Rho, Gamma and Beta sensors in our eyes determine the intensity of the colors we perceive for each of wavelengths in the visual spectrum.
  Our visual system selectively senses the range of light wavelengths that we refer to as the visual spectrum. Selective sensing of different light wavelengths allows the visual system to create the perception of color. Some people have a visual anomaly referred to as color blindness and have trouble distinguishing between certain colors. Red-green color blindness could occur if the Rho and Gamma sensor curves exactly overlapped or if there were an insufficient number of either rho or gamma sensors. A person with this affliction might have trouble telling red from green, especially at lower illumination levels.

## Slide 38: Next Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 39: Digitization
Digitization: conversion of the continuous (in space and value) electrical signal into a digital signal (digital image)
Three decisions must be made:
  Spatial resolution (how many samples to take)
  Signal resolution (dynamic range of values- quantization)
  Tessellation pattern (how to 'cover' the image with sample points)
World Optics Sensor
Signal Digitizer
Digital Representation
Notes: Let us restrict our choice of sensors to those which produce a continuous electrical signal and turn our attention to the problem of converting this signal to digital form. The process is known as digitization and sampling (also analog to digital conversion) and requires us to make three decisions:
1. What is the spatial resolution of the resulting digital image? That is, for a two-dimensional signal, how many discrete samples along the x-axis and y-axis do we want?
'sampling'
2. What geometric pattern will be used to obtain these samples?
'tessellation'
3. At each of these chosen sites, how many discrete levels of the electrical signal are required to adequately characterize the information in it?
'quantization'
In the following, we briefly consider each of these three topics.
There is a substantial amount of information about these three topics in the signal processing literature. Sub-topics include optimum parameter choice under various assumptions of the geometry, sensor choice, electrical characteristics of the sensor and the degree to which the digital signal can reconstruct the original signal.

## Slide 40: Digitization: Spatial Resolution
Let's digitize this image
  Assume a square sampling pattern
  Vary density of sampling grid
Notes: The choice of sampling interval depends largely upon the size of the structures that we wish to appear in the final digitized image. As an example, suppose we wanted to choose a sampling interval to use during the digitization of the simple house scene shown. Furthermore, suppose that it was absolutely required that the resulting digital image contain information about the picket fence around the house.

## Slide 41: Spatial Resolution
Coarse Sampling: 20 points per row by 14 rows
Finer Sampling: 100 points per row by 68 rows
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••••
Sampling interval
Sample picture at each red point
Notes: For the sake of the discussion, assume that we will use a rectangular arrangement of sample points (that is, a rectangular tessellation). We will discuss other choices of tessellation patterns later.
Note that the sampling interval determines how 'big' the resulting digital image will be. For example, if the original image is 1" by 1", and the sampling interval is .1", then the image will be sampled at 0", .1", .2",....., 1.0", for 11 sample points horizontally and 11 rows of samples vertically. Hence, the digital image will be an 11x11 array. It would be 9x9 if we don't sample the edges of the image at 0" and 1.0" or 10x10 if we start/stop sampling at .05" from the edge of the image.

## Slide 42: Effect of Sampling Interval - 1
Look in vicinity of the picket fence:
Sampling Interval:
White Image!
Dark Gray Image!
NO EVIDENCE
OF THE FENCE!
Notes: Let's look at a blowup of an area in the picket fence and consider a one-dimensional horizontal sampling. We designate the sampling interval as the distance between dots on a horizontal line. Furthermore, assume that the signal 'value' in the white area of the pickets is 100 and in the gray area between pickets it is 40.
With the sampling interval chosen, no matter where we lay the horizontal line down, the signal at adjacent dots is exactly the same. This should lead us to conjecture that the amount of resolution and detail in the digital image is directly related to how frequently the samples are taken; that is, the smaller the sampling interval, the greater the detail.

## Slide 43: Effect of Sampling Interval - 2
Look in vicinity of picket fence:
Sampling Interval:
Now we've got a fence!
What's the difference between this attempt and the last one?
Notes: Assume the same situation as on the last slide, except that now the sampling interval is exactly half what is was earlier.
Using this sampling interval, the two-dimensional 'image' now clearly shows the individual pickets as well as the house wall behind the fence. What is the difference between these two results?

## Slide 44: The Missing Fence Found
Consider the repetitive structure of the fence:
Sampling Intervals
Case 1: s' = d
The sampling interval is equal to the size of the repetitive structure
NO FENCE
Case 2: s = d/2
The sampling interval is one-half the size of the repetitive structure
FENCE
Notes: Assume that the distance from the center of one picket to the center of the next is d. Furthermore, let's assume that the width of the pickets and the width of the holes is the same.
In the first case, the sampling interval is equal to the size of the repetitive structure and consequently it does not show up in the final result.
In the second case, the sampling interval is half the size of the repetitive structure and the fence becomes visible.
This should lead us to further conjecture that, in order to assure that a repetitive structure of size d appears in the final image, the size of the sampling interval should be d/2.
What would happen if the sampling interval was set to 3d/4? If it was d/4?

## Slide 45: The Sampling Theorem
IF: the size of the smallest structure to be preserved is d
THEN: the sampling interval must not be larger than d/2
Can be shown to be true mathematically
Repetitive structure has a certain frequency
  To preserve structure must sample at twice the frequency
  Holds for images, audio CDs, digital television….
Leads naturally to Fourier Analysis (optional)
Notes: The formal statement of the conjecture relating the size of the repetitive structure and the sampling interval is known as the sampling theorem. The sampling theorem says that if the size of the smallest structure to be preserved in the image is d, then the sampling interval must be smaller than 1/2 d.
This can be shown to be true mathematically. The proof involves interpreting d (the picket spacing here) as a period of repetition, thus relating it to a frequency. In the ideal case, a signal (or image) has a limit to how high this frequency can be or alternately, a limit on how closely spaced the repetitive structure will be. Any such signal is called 'band-limited'. It can be shown that any bandlimited signal can be completely characterized by a discrete sampling whose spacing is less than or equal to some minimum spacing. This minimum sampling rate is called the Nyquist rate. In this case, a complete characterization means that the original signal may be reconstructed exactly from the samples. Furthermore, sampling at a rate higher than the Nyquist rate serves no additional purpose.
The sampling theorem has application well beyond computer vision, since it applies to any continuously varying signal. In fact, a good example of its application is in the area of digital music reproduction (e.g. CD players and digital audio tape players). The human ear typically hears sounds in the range of 200 hertz (Hz) to about 20 KHz. In order to reproduce this signal exactly, the musical signal must be sampled at a minimum of 40,000 samples per second (40KHz); this is the Nyquist rate. Consequently, you often see '2x oversampling' displayed on CD players. To account for the variability of frequency sensitivity among listeners, and for other complications in sound reproduction, sampling rates of twice the minimum theoretically necessary rates (4x) or four times the minimum (8x) sampling rates are often used. Hence, '4x or 8x oversampling' is also commonly seen on CD players and digital audio tape players. Sampling more frequently than this does not improve the quality of the music, since the human ear cannot hear the distinction.

## Slide 46: Sampling
Rough Idea: Ideal Case
Dirac Delta Function 2D "Comb"
"Continuous Image"
"Digitized Image"
d(x,y) = 0 for x = 0, y= 0
d(x,y) dx dy = 1
f(x,y)d(x-a,y-b) dx dy = f(a,b)
d(x-ns,y-ns) for n = 1….32 (e.g.)
23
s

## Slide 47: Sampling
Rough Idea: Actual Case
  Can't realize an ideal point function in real equipment
  "Delta function" equivalent has an area
  Value returned is the average over this area
23
s

## Slide 48: Mixed Pixel Problem
Notes: This 'averaging effect' is not what we'd like to see during sampling. Consider the image of the mushroom and the background. If we blow up a small area on the periphery of the mushroom, the effect of this averaging process is very clear. The transition from the background to the mushroom is not a sharp one. The pixels along the boundary of the mushroom represent averages of part of the background and part of the mushroom, because the sampling area overlapped both of them.
This is called the mixed-pixel problem in vision and arises because of the finite sampling area. Unfortunately, there is little that can be done to improve the situation. It will return to haunt us when we talk about the extraction of edges and regions from images and when we talk about automatic methods of classifying images.

## Slide 49: Signal Quantization
Goal: determine a mapping from a continuous signal (e.g. analog video signal) to one of K discrete (digital) levels.
I(x,y) = .1583 volts
= ????
Digital
value
Notes: The choice of a tessellation and the horizontal and vertical sampling intervals impose a regular structure of points (or, as we've seen, areas) on the image plane which define the locations where the electrical signal (which is proportional to image irradiance) from the sensor will be measured. This signal is also continuous and must be mapped onto a discrete scale (or quantized). Assume that the output voltage of a video camera varies from 0 volts (completely black) to 1 volt (representing the brightest white the camera can reliably detect). This continuous range (0-1) must be mapped onto a discrete range (say 0,1,2,....,k-1). For example, what does the signal value .1583 volts measured at location (10,22) mean in terms of the digital image?
______________________note____________________________
Since the dynamic range of video cameras is fairly small, and they must be used in a wide variety of situations, such as indoors under artifical illumination to bright sunlit outoor scenes, camera typically have one or mechanisms for controlling the amount of light reaching the sensor. For example, variable f-stops are usually built into the lens and automatic gain controls are often built into the camera electronics. If the measured sensor signal must be quantitatively related to the image irradiance, these factors must be taken into consideration. Note that neither of these 'add-ons' improve the intrinsic dynamic range of the sensor; they simply permit the sensor to operate over widely varying illumination levels.

## Slide 50: Quantization
I(x,y) = continuous signal: 0 ≤ I ≤ M
Want to quantize to K values 0,1,....K-1
K usually chosen to be a power of 2:
Mapping from input signal to output signal is to be determined.
Several types of mappings: uniform, logarithmic, etc.
K #Levels #Bits
2 2 1
4 4 2
8 8 3
16 16 4
32 32 5
64 64 6
128 128 7
256 256 8
Notes: The problem is to define the levels to quantize the continuous signal to. If we let I(x,y) be the continuous signal, I is typically bounded by some upper and lower bounds (say 0 and M) on the strength of the signal and hence the range [0,M] must be mapped into K discrete values. Typically, K is chosen to be a power of 2. The rationale behind this choice has to do more with the utilization of image memory than with any theory of quantization. Thus, if we choose K = 16, 16 gray levels can be represented in the final image and this can be done in 4 bits. If we choose K = 256, then there are 256 gray levels in the final image and each pixel can be represented in 8 bits.
In a color image represented by R, G, and B images, the signal level for each image is typically quantized into the same number of bits,although in some compression schemes more bits are allocated to green, for instance, than to red or blue.
The situation regarding the choice of K is similar to our previous discussion on selection of the sampling interval in that it affects how faithfully the quantized signal reproduces the original continuous signal. Typically, a high value of K allows finer distinctions in the grey level transitions in the original image, up to the limit of noise in the sensor signal. In many cases, K=128 (7 bits) or 256 (8 bits) and we are forced to live with the final result.

## Slide 51: Choice of K
Original
Linear Ramp
K=2
K=4
K=16
K=32
Notes: The original image is a linear ramp, running from 0 (black) to 256 (white). It is actually a digital image quantized with K=8. We can re-quantize this into a smaller range. Choosing K=2 results in a binary image which has lost all of the effect of a ramp; the quantized image looks like a step function. Choosing increasingly larger values of K results in a larger number of gray levels with which to represent the original. The stripes get narrower and eventually, with a large enough value of K, look like a continuous image to the eye. The artificial boundaries induced by the requantization are called false contours and the effect is called gray scale contouring. This was seen fairly frequently in earlier digital cameras when photos were taken which contained areas of slow color or intensity gradients.

## Slide 52: Choice of K
K=2 (each color)
K=4 (each color)

## Slide 53: Choice of Function: Uniform
Uniform quantization divides the signal range [0-M] into K equal-sized intervals.
The integers 0,...K-1 are assigned to these intervals.
All signal values within an interval are represented by the associated integer value.
Defines a mapping:
Notes: Prior to quantizing the signal, it can be 'shaped' by applying a function to the original continuous values. There are several popular choices for the quantization function. The first is simply a linear ramp; quantization using this function is called Uniform Quantization. Here, the range of the continuous signal (0 to M) is broken up into K equal sized intervals. Each interval is represented by an integer 0 to K-1; these integer values represent the set of possible gray values in an image quantized using this method. All values of the continuous signal V(x,y) falling within one of the K intervals are represented by the corresponding integer.
If the original scene contains a fairly uniform distribution of 'brightnesses', then uniform quantization ensures that the distribution of discrete gray levels in the digital image is also uniformly distributed. Another way is saying this is that all of the 0 to K-1 gray levels are used equally frequently in the resulting digital image.

## Slide 54: Logarithmic Quantization
Signal is log I(x,y).
Effect is:
Detail enhanced in the low signal values at expense of detail in high signal values.
Notes: In those cases where the continuous signal is not uniformly distributed over the range 0 to M, it is possible to choose a quantization function such that the resulting digital gray levels are uniformly distributed. A uniform distribution is often the goal of quantization, since then each of the gray scale values 0 to K-1 are 'equally used'. For example, if we knew a priori that the values of the continuous signal were logarithmically distributed toward the low end of the range, we could choose a logarithmic quantization function such as the one shown. This has the effect of providing more discrete gray levels in the low end of the continuous range and fewer towards the high end. The lower levels are enhanced and the higher levels are compressed.
There is some evidence that the human eye uses a type of logarithmic mapping.
Many image processing systems allow the user to define arbitrary mapping functions between the original signal and the discrete range of gray values 0 to K-1.

## Slide 55: Logarithmic Quantization
Original
Logarithmic Quantization
Quantization Curve
Notes: The quantization curve shown (from Adobe Photoshop) was hand drawn to approximate a logarithmic curve. Note how the details in the shadows under the mushrooms are enhanced because of the larger number of values available at the dark end of the scale.

## Slide 56: Tesselation Patterns
Hexagonal
Triangular
Rectangular
Typical
Notes: In order to obtain a digital image from a continuous sample, there were three things we had to specify:
1. The spatial resolution of a quantized sample.
2. The quantization function and number of discrete levels.
3. The tessellation pattern of the image plane.
Ideally, we should choose a tessellation pattern which completely covers the image plane. There are many possible patterns which do this, but only the regular ones are of interest here - these include the square, the triangle, and the hexagon. The square pattern is the one most widely used, even though the actual scanning area is more elliptical in shape. The triangular pattern is hardly ever used. The hexagonal pattern has some interesting properties which will become apparent as we discuss digital geometry.

## Slide 57: Lecture Outline
Image Formation Basic Steps
Geometry
  Pinhole camera model & Thin lens model
  Perspective projection & Fundamental equation
Radiometry
Photometry
  Color, human vision, & digital imaging
Digitalization
  Sampling, quantization & tessellations
More on Digital Images
  Neighbors, connectedness & distances

## Slide 58: Digital Geometry
Neighborhood
Connectedness
Distance Metrics
Picture Element or Pixel
Pixel value I(i,j) =
0,1 Binary Image
0 - K-1 Gray Scale Image
Vector: Multispectral Image
32
I(i,j)
(0,0)
i
j
Notes: We now turn our attention to the familiar concepts of geometry, such as distances between points, but from the point of view of a digital image.
A digital image, as already noted, can be thought of as an integer-valued array whose entries are drawn from the finite set {0...K-1}. Each entry in this array is called a 'picture element' or pixel. Each pixel has a unique 'address' in the array given by it's coordinates (i,j). The value at location (i,j) is the quantized value of the continuous signal sampled at that spatial location.
If K=2, the image is called a binary image, since all gray levels are either 0 or 1. For K>2, the image is called a grayscale image for the obvious reasons. When the value at a particular spatial location is a vector (implying multiple images), then the image is called a multispectral image. For example, a color image can be thought of as an image in which the value at a single pixel has three components (for each of the red, green, and blue components of the color signal) represented as a three element vector.

## Slide 59: Connected Components
Binary image with multiple 'objects'
Separate 'objects' must be labeled individually
6 Connected Components
Notes: Let's consider the concept of 'connectedness' in an image represented in discrete form on a rectangular grid. The simple binary image shown contains four 'objects': a central object that looks like a blob, a ring completely encircling it, and a second blob in the lower right hand corner, all represented by white pixels. The fourth object is the background, represented by black pixels. One would like to say that all the pixels in one of these objects are connected together and that the objects are not connected to each other or the background.
In this image, there are six connected components: the three objects and the three pieces of the background. All of the pixels in the ring, for example, share several features: they are all white, taken together they form the ring, and, for every pixel in the ring, a path can be found to every other pixel in the ring without encountering any 'non-ring' pixels. This latter feature illustrates the concept of connectedness in a digital image; its definition can be made much more precise.

## Slide 60: Finding Connected Components
Two points in an image are 'connected' if a path can be found for which the value of the image function is the same all along the path.
P1
connected to
P2
P3
connected to
P4
P1
not connected to
P3 or P4
P2
not connected to
P3 or P4
P3
not connected to
P1 or P2
P4
not connected to
P1 or P2
Notes: By definition, two pixels in an image are connected if a path from the first point to the second point (or vice-versa) can be found such that the value of the image function is the same for all points in the path. It remains to be defined exactly what is meant by a 'path'.

## Slide 61: Algorithm
Pick any pixel in the image and assign it a label
Assign same label to any neighbor pixel with the same value of the image function
Continue labeling neighbors until no neighbors can be assigned this label
Choose another label and another pixel not already labeled and continue
If no more unlabeled image points, stop.
Who's my neighbor?
Notes: Given a binary image, its connected components can be found with a very simple algorithm. Pick any point in the image and give it some label (say A). Examine the neighbors of the point labeled A. If any of these neighboring points have the same gray value* (here, only 0 or 1 are possible gray values), assign these points the label A also. Now consider the neighbors of the set of points just labelled; assign the label A to any which have the same gray value. Continue until no more points can be labelled A. The set of pixels labelled A constitute one connected component, which was 'grown' from the central point that was originally labelled. Now pick any point in the image which has not been labelled and assign it a different label (say B) and grow out from it. Repeat the process of picking an unlabelled point, assigning it a unique label, and growing out from this point until there are no unlabelled points left in the image. Eventually, every image pixel will have been assigned a label; the number of unique labels corresponds to the number of connected components in the image.
Any pixel in a connected component is 'connected' to every other pixel in the same connected component but not to any pixel in a connected component with a different label. It is clear, therefore, that the notion of 'connectedness' in an image is intimately related to the definition of a pixel's neighbors. Let's explore the idea of the neighborhood of a pixel and the idea of the neighbors of a pixel in a little more detail.
But first, let's illustrate this algorithm with an example.
___________________
* Or color or texture or whatever other feature we are interested in.

## Slide 62: Example
Notes: To illustrate the simple connected components algorithm, choose the top left pixel (arbitrary decision) and label it blue. This pixel has three neighbors, only two of which have the same gray level - the one to its immediate right and the one below it; label them both blue. In the next step, consider these two just-labeled points, starting with the right one. This point has 5 neighbors, one of which is our original point (already labeled) and one of which was labeled in the previous step. Of the three remaining pixels, only one has the same gray level, so label it blue. Now consider the second pixel labeled in the second step (just below the original start point). This pixel also has five neighbors, two of which are already labeled. Of the three remaining pixels, two have the same gray level and can therefore be labeled blue. This ends the third application of the growing process. Repeating this until no further pixels can be labeled results in the connected component shown in blue in the leftmost image of the middle row. Now pick any unlabeled point in the original image and start all over again.
At the end of the process, the image has been decomposed into five connected components. Connected component labeling is a basic technique in computer vision; we will repeatedly use this and similar algorithms throughout the remainder of the course.

## Slide 63: Neighbor
Consider the definition of the term 'neighbor'
Two common definitions:
Consider what happens with a closed curve.
One would expect a closed curve to partition the plane into two connected regions.
Four Neighbor
Eight Neighbor
Notes: In defining the notion of a path, and in the connected components algorithm, we used the term 'neighbor' in a very intuitive way. Let's examine this intuition a little more closely. There are two obvious definitions of neighbor and neighborhood commonly used in the vision literature. The first of these is called a 4-neighborhood; under this definition, the four pixels in gray surrounding the blue pixel are its neighbors and the blue pixel is said to have a neighborhood composed of the four gray pixels. These pixels are 'connected' to the blue pixel by the common edge between them. The second definition is called an 8-neighborhood and is shown on the right; the 8 neighbors of the blue pixel includes the four edge-connected neighbors and the four vertex connected neighbors.
Neither of these definitions is entirely satisfactory for the definition of a neighborhood. Consider the digital counterpart of a closed curve in the plane, which partitions the background into two components........

## Slide 64: Alternate Neighborhood Definitions
Notes: Suppose we have a closed curve in a plane. One of the properties of a closed curve is that it partitions the background into two components, one of which is inside the curve and one of which is outside the curve. The top image represents a digital version of such a curve. Let's apply the two definitions of 'neighborhood' to it and analyze what happens to the curve and the background in terms of their connectedness.
Let's consider the 4-neighborhood definition first. In this case, the diagonally connected pixels that make up the 'rounded' corners of the O are not connected. Hence, the O is broken into four distinct components. The curve we said was connected is not connected using the 4-neighborhood definition of a neighborhood. On the other hand, the background pixels are not connected across the diagonally connected points either, so the background is broken into two separate connected components. We are now in the curious position of having the background partitioned into two parts by a curve that is not connected (or closed).
Now consider the 8-neighborhood definition. In this case, the O is connected, since the vertex connected corners are part of the neighborhood. However, the inside and outside background components are also connected (for the same reason). We now have a closed curve which does not partition the background!

## Slide 65: Possible Solutions
Use 4-neighborhood for object and 8-neighborhood for background
  requires a-priori knowledge about which pixels are object and which are background
Use a six-connected neighborhood:
Notes: One possible solution to this dilemma is to use the 4-connected definition for objects and the 8-connected definition for the background. Of course, this implies that we must know which points correspond to the object and which parts correspond to the background. In general, the separation into object and background is not known a priori.

## Slide 66: Digital Distances
Alternate distance metrics for digital images
Euclidean Distance
City Block Distance
Chessboard Distance
= (i-n) 2 + (j-m) 2
= |i-n| + |j-m|
= max[ |i-n|, |j-m| ]
Notes: In many cases, it is necessary to measure the distance between two points on the image plane. There are three metrics commonly used in vision. First, the standard Euclidean distance metric is simply the square root of the sum of the squares of the differences in the coordinates of the two points. The computation of this metric requires real arithmetic and the calculation of a square root; it is computationally expensive, but the most accurate.
An approximation to the Euclidean distance is the city block distance, which is the sum of the absolute values of the differences in coordinates of the two points. The city block distance is always greater than or equal to the Euclidean distance.
The third metric is called the chessboard distance, which is simply the maximum of the absolute values of the vertical and horizontal distances.
These last two metrics have the advantage of being computationally simpler than the Euclidean distance. However, for precise mensuration problems, the Euclidean distance must be used. In other cases, the choice of the metric to use may not be as critical.

## Slide 67: Next
Next:
Feature Extraction
Homework #1 online